MINIMUM SPECIFICATIONS FOR BOSS BULLET 2

Quantity of one (1) Boss model BULLET 2 portable air compressor (s) to include the following as standard equipment:

COMPRESSOR:

- Boss oil-flooded, rotary screw air-end designed to produce up to 70 CFM @ 100 PSIG continuously.

- Two-year warranty on the air-end.

- Vertical air/oil reservoir with filler port and sightglass.  Bolt on lids and/or end plates not acceptable.

- Self-contained separator element with easy access spin-on housing.

- Aerodynamically designed cooling package with automatic thermal sensing control to ensure proper operating temperatures.

- Replaceable spin-on compressor lubricant filter with safety bypass and 25 micron rating.

- Dry-type air intake filter with replaceable element.

- Instrumentation to include:  hourmeter and air pressure gauge, keyed off /on switch and choke.

- Safety devices to include:  minimum pressure device, compressor lube hi-temp, automatic blowdown device, high-pressure relief valve, and necessary warning and information decals.

- Frame and canopy with easy access doors.

- 5 Gallon E.P.A / C.A.R.B. approved fuel tank.

- Dimensions not to exceed: 45”L x 20”W x 30”H

- Operation, parts, and maintenance manual.

ENGINE:

- Kohler CH-730 25 Hp, 4-cycle, v-twin, overhead valve, air-cooled gasoline engine.

- Two-year warranty on engine.

- Electronic ignition for broad RPM response.

- Cast-Iron cylinder liners for power and durability.

- 2013 E.P.A. & C.A.R.B. small engine certified.

- Overhead valve design for greater fuel efficiency and lower emissions.

- In line fuel filter.

- Oil fill in valve cover.

- Carburetor w/solenoid fuel shutdown for all weather consistent starting.

- Replacement dry element air cleaner with polyurethane wrapper.

- Rotating blower screen.

- Low oil pressure switch with safety shutdown.

- Muffler heat shield & guard.

- Oil cooler for heavy-duty power demands.

- Hydraulic valve lifter.

- 25 amp charging system.

OPTIONAL:

- Wheel mount with third wheel caster.

- Dual Pressure

- Remote stop/start/choke